## Slide 1: Algorithmic SDN Programming: Toward High-Level SDN Programming
Y. Richard Yang
Dec. 3, 2015
Notes: What does it mean to say software-driven? For large network equipment vendors, software cost already accounts for 90% of R&D cost.

## Slide 2: What is SDN?
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 3: What is SDN: a “Main-Stream” View
Separation of data and control paths, with a logically centralized control plan
Datapath
Control
Datapath
Control
Datapath
Control
Traditional
Datapath
Datapath
Control
Datapath
SDN
standard control
protocol
Notes: FLP, Arrow’s Impossibility Theorem. Failure of distributed computing.

## Slide 4: An Evolution View of Intradomain Routing Toward SDN
Distance Vector
Datapath
Distributed Bellman Ford
Distributed Link State
Dijkstra
Logically Central Link State
Control
Datapath
Distributed Bellman Ford
Datapath
Distributed Bellman Ford
Distributed Link State
Distributed Link State
Dijkstra
Dijkstra
Link State
SDN
Notes: RIP: 1988 RFC1058 RFC2328

## Slide 5: Why SDN (A “Defeatist” View)?
Distributed computing is hard, e.g.,
  FLP Impossibility Theorem
  Arrow’s Impossibility Theorem
Achieved good design for only some specific tasks (e.g., state distribution, leader election). Hence, one can consider SDN as a way of moving away from generic distributed computing, by focusing on utilizing the few well-understood primitives, in particular logically centralized state.

## Slide 6: What is SDN: a “Whitebox”/Programmable-Network View
Separation of switch hardware and software
HardwareB
SoftwareB
HardwareA
SoftwareA
Traditional
HardwareC
SoftwareC
HardwareB
SoftwareC
HardwareA
SoftwareC
Whitebox
HardwareA
SoftwareD
Notes: FLP, Arrow’s Impossibility Theorem. Failure of distributed computing.

## Slide 7: Why SDN or More Programmable Networks?
Modern networks contain increasingly more diverse types of equipment
In traditional settings, each type/vendor runs in its own hardware box
Substantial flexibility if more programmable nets
Source: [Sherry, et. al SIGCOMM’12]
Small: <=1k hosts; Medium: 1k-10k; Large: 10k-100k; Very Large: >= 100k
Notes: 为啥呢？因为total ownership cost少。1. 我server买了，3年合同以后可以自行切换。前三年load cisco的virtual router，后三年load juniper的virtual switch。再过三年load palo alto的virutal firewall 2. 设备performance更新，只需要换低层硬件，就可以扩展
Router, switch, firewall merge
  Server + software, which include Router, Switch, FT
DC -> Cloud
  ENT switch reducing; Cloud increasing
There are more virtual ports than physical ports, where the virtual ports are controlled by x86 software. Where software erodes hardware

## Slide 8: Why SDN or More Programmable Networks?
Network customization/feature requests can be a slow process. Open/programmable systems introduce competition and may allow more innovation.
Notes: small (fewer than 1k hosts), medium (1k-10k hosts), large (10k-100k hosts), and
very large (more than 100k hosts) enterprise network

## Slide 9: More Programmable Networks are a Well Recognized Trend
“We are focusing on a market transition involving the move toward more programmable, flexible, and virtual networks… This transition is focused on moving from a hardware-centric approach for networking to a virtualized network environment that is designed to enable flexible, application-driven customization of network infrastructures. -- Cisco Annual Report (pp2), Nov. 2015
Notes: “The cost to operate networks is too high and growing too fast and you can’t find enough people to manage these things anymore. It’s time for change.” -- Nick Lippis, ONUG /Fidelity, 2013
To appeal to companies looking for more highly customized systems, Cisco has also opened up its software to programmers in new ways, making it easier for clients to write their own apps for Cisco products.
http://www.bloomberg.com/news/articles/2015-11-05/cisco-s-new-ceo-embraces-the-cloud

## Slide 10: What is SDN: A New Control-Plane Abstraction View
Major advances in many fields of computer science are based on simple, powerful abstractions
  “Modularity based on abstraction is the way things get done.” -- Barbara Liskov
A major lacking of networking is that we do not have enough good abstractions in network control plane
  Three key areas for abstractions [Shenker’11]: Distribution, configuration, and forwarding
Notes: Hide details; Provide automatic optimization
Theory: Turing machine; systems: DB/relational algebra; OS/Virtual memory/thread; PL: low level language to higher level languages. Networking layer architecture is abstractions for data plane. Major advance is possible if we introduce the right abstractions in the network control plane.

## Slide 11: Our Goal
Realize one key benefit of SDN: Better programming abstractions, tools to allow easier, more efficient, more robust (secure), high-level network control and management.
Notes: Benefits of abstraction: hide details, automatic instead of manual optimization, hide dynamics, hide resource limitations.

## Slide 12: Some Main Current Use Cases of SDN
Source: Neela Jacques, July 2015.
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 13: Outline
What and why SDN?
Current SDN programming systems
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 14: State of Current (Open Source) Players
Source: Neela Jacques, July 2015.

## Slide 15: OpenDaylight Architecture
Controller
Model-Driven SAL (MD-SAL)
Protocol Plugin
RESTCONF
NETCONF SERVER
Network Devices
Applications
App/Service Plugin
App/Service Plugin
...
...
Protocol Plugin
Config Subsystem
Messaging
Data Store
Remote Controller Instance
Remote Controller Instance
Network Applications Orchestration & Services
Controller Platform
Plugins & Applications
Clustering
Network Devices
Network Devices
Applications
Applications
Source: Ed Warnicke, July 27, 2015.
15

## Slide 16: OpenDaylight Architecture
https://wiki.opendaylight.org/view/OpenDaylight_Controller:Architectural_Framework

## Slide 17: ONOS Architecture
https://wiki.onosproject.org/display/ONOS/System+Components
Notes: http://api.onosproject.org/1.1.0/org/onosproject/store/Store.html DeviceStore, HostStore, LinkStore, TopologyStore collect info from below
FlowRuleStore supports forwarding abstractions
IntentStore

## Slide 18: An Abstract View: Focus of Current SDN Systems is Data Store (Distribution)
Network View
NE Datapath
Service/ Policy
NE Datapath
logically centralized data store

## Slide 19: What is Missing?
Network View
NE Datapath
Service/ Policy
NE Datapath
logically centralized data store
Program

## Slide 20: Datapath Model
Low-level TCAM based computing model with limited resources

## Slide 21: Example: A Simple SDN Controller
badPort = 22 // policy hostTbl = {A:1,B:2, C:3,D:4} // net view
def onPacketIn(p):
if badPort == p.tcp_dst: drop
else: forward([hostTbl(p.eth_dst)])
C
D
A
B
1
2
3
4
Notes: SDN is a recent hot topic. During a recent NSF panel, many proposals are on SDN. A common feedback is if a propsal can be related with SDN.

## Slide 22: Controller Program with Flow Table Management
hostTbl = {A:1,B:2,C:3,D:4}
def onPacketIn(p):
if 22 == p.tcp_dst: drop
installRule({‘match':{'tcp_dst':22}, ‘action’:[]})
else: forward([hostTbl(p.eth_dst)])
installRule({‘match’: {‘eth_dst’:p.eth_dst, ’tcp_dst’!=22},
‘action’:[hostTbl(p.eth_dst)]})
Notes: SDN is a recent hot topic. During a recent NSF panel, many proposals are on SDN. A common feedback is if a propsal can be related with SDN.

## Slide 23: Controller Program with Flow Table Management
hostTbl = {A:1,B:2,C:3,D:4}
def onPacketIn(p):
if 22 == p.tcp_dst: drop
installRule({‘priority’:1, ‘match’:{'tcp_dst':22}, ‘action’:[]})
else: forward([hostTbl(p.eth_dst)])
installRule({‘priority’:0, ‘match’: {‘eth_dst’:p.eth_dst},
‘action’:[hostTbl(p.eth_dst)]})
Notes: SDN is a recent hot topic. During a recent NSF panel, many proposals are on SDN. A common feedback is if a propsal can be related with SDN.

## Slide 24: Does the Program Work?
Controller
Switch
def onPacketIn(p):
if 22 == p.tcp_dst: drop
installRule({`priority`:1,’match’:{‘tcp_dst':22},'action':[]})
else:
installRule({`priority`:0,’match’:{‘eth_dst’:p.eth_dst},
'action':[hostTbl(p.eth_dst)]})
forward([hostTbl(p.eth_dst)])
EthDst:A,
TcpDst:80
{`priority`:0,’match’:{‘eth_dst’:A},'action':[1]}
EthDst:A,
TcpDst:22
Notes: Unfortunately, this program has a bug. To see where the program goes wrong, let’s watch what happens when we connect this controller to a single switch and let two packets arrive. Both packets have destination mac A. The red packet is to TCP destination 80, while the green packet is to TCP destination 22. When the red packet arrives, the switch has an empty flow table and sends the packet to the controller. The controller determines that the packet should be forwarded to the next hop, and installs the appropriate rule. The red packet returns to the switch and moves onward. Now, the port 22 packet arrives at the switch, and instead of being dropped or sent to the controller, it matches the low priority rule for Ethernet destination A and is therefore forwarded onward. This violates the user’s intentions and may represent a security violation.

## Slide 25: Approach I (OVS): Using Exact Match
hostTbl = {A:1,B:2,C:3,D:4}
def onPacketIn(p):
if 22 == p.tcp_dst: drop
installRule({‘priority’:1, ‘match’:exactMatch(p), ‘action’:[]})
else: forward([hostTbl(p.eth_dst)])
installRule({‘priority’:0, ‘match’:exactMatch(p),
‘action’:[hostTbl(p.eth_dst)]})
Notes: SDN is a recent hot topic. During a recent NSF panel, many proposals are on SDN. A common feedback is if a propsal can be related with SDN.

## Slide 26: Problems of Approach I
Each new TCP flow delayed for flow setup (10-100 ms)
Number of flow table rules may exceed capacity (typically a few thousands)

## Slide 27: Approach 2: Declarative Policy Languages
if_(match(dstport(22)), drop,
if_(match(dstmac=EthAddr(a)), fwd(1),
if_(match(dstmac=EthAddr(b)), fwd(2),
if_(match(dstmac=EthAddr(c)), fwd(3),
if_(match(dstmac=EthAddr(d)), fwd(4),
flood() )))))
Probably the most well-known is Pyretic [NSDI’13]
Notes: SDN is a recent hot topic. During a recent NSF panel, many proposals are on SDN. A common feedback is if a propsal can be related with SDN.

## Slide 28: Outline
What and why SDN?
Current SDN programming systems
Algorithmic SDN programming
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 29: Goal
Can we let programmers write the most obvious (=> data path independent) code:
… and we automatically generate correct, highly-optimized data path?
def onPacketIn(p) if 22 == p.tcp_dst: drop
else: forward([hostTbl(p.eth_dst)])
Notes: SDN is a recent hot topic. During a recent NSF panel, many proposals are on SDN. A common feedback is if a propsal can be related with SDN.

## Slide 30: Big Picture: Before
Switches
User Level
Under the hood
Controller Library
Step 1. Make Decisions
Step 2. Generate Rules
Notes: So today, Openflow programmers are responsible for deciding both how to forward packets and how to configure flow tables. We observe that programmers will be motivated by performance goals to use wildcard rules and that reasoning about wildcard rules is complex and introduces a substantial risk of misconfiguration.

## Slide 31: Big Picture: After
Step 1. Make Decisions
OF Switches
OF Controller Library
Step 2. Generate Rules
User Level
Under the hood
Notes: Therefore, we ask whether it is possible to fully automate the generation of high quality flow tables, thereby removing this task from the programmer’s responsibility, simplifying their programs and eliminating this source of errors.
We call the remaining part of the user’s program, an “algorithmic policy”.

## Slide 32: Algorithmic SDN Programming Abstraction: User’s View
Conceptually network control function f is invoked on every packet entering the network.
f expressed in a general purpose language (e.g., Java, Python), describing how a packet should be routed, not how data path flow tables are configured
f: packet route
Notes: ...
Where packet provides access to packet attributes, env provides access to environment state, such as topology and host locations, and the route can be a unicast route, a null route or a multicast route.
...

## Slide 33: Example Algorithmic Policy in Java
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc = hostTable(p.ethSrc());
Location dloc = hostTable(p.ethDst());
Route path = myRoutingAlg(topology(), sloc,dloc);
return path;
}
}
Route myRoutingAlg(Topology topo, Location sLoc, Location dloc) {
if ( isSensitive(sLoc) ) return secureRoutingAlg(topo, sloc, dloc);
else return standardRoutingAlg(topo, sloc, dloc);
}
Does not specify anything on flow tables!
Notes: Here is an example algorithmic program, written in Java.
Explain program.
Note that the program does not specify flow table configuration.
So the programming model makes the programmer’s life easy: just take a packet and say what to do with it.

## Slide 34: Outline
Current SDN programming systems
Algorithmic SDN programming
  Programming model
  Maple
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 35: Maple: Challenge and Basic Idea
Challenge: How is it possible that one can derive datapath (flow-tables) from a datapath-oblivious controller function f?
Basic idea:
  There are representations of computation
    A sequence of instructions (whitebox)
    Memorization tables (blackbox)
  Although the decision function f does not specify how flow tables are configured, if for a given decision (e.g., drop), we know the dependency of the decision, we can construct the flow tables (aka, memorization tables).
Notes: ...
Where packet provides access to packet attributes, env provides access to environment state, such as topology and host locations, and the route can be a unicast route, a null route or a multicast route.
...

## Slide 36: Maple: Basic Idea
Only requirement: Programs use simple library to access pkt attributes:
Library provides both convenience and more importantly, decision dependency!
Notes:   - Switches have limited TCAM capacity for rules; hence, craft rule sets to optimize TCAM utilization.
  - Generated rules may become invalid when network or policy state changes. Need to detect and repair inconsistency with minimal disruption.
  - Some policies are inherently hard to distribute and generate many central executions.
On the other hand implementing algorithmic policies is challenging.
We know that naive solutions -- process every packet at controller or use only exact match rules -- perform poorly.
Static analysis to determine layout of flow tables is possible, but has drawbacks; in particular static analysis of general purpose language programs is typically conservative. Furthermore, relying on static analysis will cause the system to become substantially dependent on the source language in which we write algorithmic policies.

## Slide 37: Dynamic Tracing: Abstraction to Flow Tables
1. Observes decision dependency of f on pkt attributes.
2. Builds a trace tree (TT), a universal (general), partial decision tree representation of any f.
3. Compile trace tree to generate flow tables (FTs).
Notes: Instead, we introduce Maple, a system that implements algorithmic policies using a fully dynamic compilation method and which does not depend on the source language used to express the algorithmic policy.
Maple works by repeatedly executing the user’s algorithmic policy f on packets entering the network, generalizing the outcome to other packets by observing traces of data accesses made during the execution.
Maple then accumulates these traces into a trace tree, which is a partial decision tree of the input algorithmic policy, f.
Finally, Maple compiles flow tables (FTs) for all the switches in the network from the trace tree. The compilation is done so that packets for which Maple has not yet successfully inferred a forwarding decision are sent back to the controller to ensure that Maple continues to execute f and refine its trace tree.

## Slide 38
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc =
hostTable(p.ethSrc());
Location dloc =
hostTable(p.ethDst());
Route path =
myRoutingAlg(
topology(),sloc,dloc);
return path;
}
}
EthSrc:1,
EthDst:2,
TcpDst:80
Assert: TcpDst==22
false
Read: EthSrc
Read: EthDst
1
2
Policy
path1
Notes: We use the example Java algorithmic policy to illustrate the tracing method. Suppose Maple executes the algorithmic policy on a packet with Ethernet source 1, Ethernet dest 2 and tcp destination 80. As the packet moves through the policy, Maple collects a trace of the execution.
When this packet arrives at the check on tcp destination, Maple records the assertion, and its outcome. In this case, the outcome is false. The program proceeds to the else branch, where it reads the source and destination addresses, both of which Maple logs. Finally, the program returns the computed path.

## Slide 39
EthDst:1,
TcpDst:22
null
true
Assert: TcpDst==22
Policy
Trace Tree
1
2
?
true
false
Read: EthSrc
Read: EthDst
path1
Assert: TcpDst==22
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc =
hostTable(p.ethSrc());
Location dloc =
hostTable(p.ethDst());
Route path =
myRoutingAlg(
topology(),sloc,dloc);
return path;
}
}
Notes: Maple then uses this trace to begin generating the Trace Tree. In this case, Maple still doesn’t know what will happen if the assertion is true, and it therefore adds a placeholder under the true branch.
Now, if we execute f on a packet to tcp destination 22, the assertion is true, and the packet is dropped. Maple logs this new trace and uses it to refine its Trace Tree, filling in the true branch of the assertion.

## Slide 40
EthDst:1,
TcpDst:22
null
true
Assert: TcpDst==22
Policy
Trace Tree
1
2
null
true
false
Read: EthSrc
Read: EthDst
path1
Assert: TcpDst==22
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc =
hostTable(p.ethSrc());
Location dloc =
hostTable(p.ethDst());
Route path =
myRoutingAlg(
topology(),sloc,dloc);
return path;
}
}
Notes: Maple then uses this trace to begin generating the Trace Tree. In this case, Maple still doesn’t know what will happen if the assertion is true, and it therefore adds a placeholder under the true branch.
Now, if we execute f on a packet to tcp destination 22, the assertion is true, and the packet is dropped. Maple logs this new trace and uses it to refine its Trace Tree, filling in the true branch of the assertion.

## Slide 41: Trace Tree Formal Spec
A tree w/ 4 types of nodes
  T node: assertion on packet attributes
  V node: multi-way branching on a packet attribute
  L node: leaf node labeled w/ action
  ? node: unknown
TT search: traverse tree for a given packet to determine action or no answer
TT correctness: if TT records an answer for a given packet, the answer is the same as the original algorithm
1
2
?
true
false
Read: EthSrc
Read: EthDst
path1
Assert: TcpDst==22
Notes: On the other hand implementing algorithmic policies is challenging.
We know that naive solutions -- process every packet at controller or use only exact match rules -- perform poorly.
Static analysis to determine layout of flow tables is possible, but has drawbacks; in particular static analysis of general purpose language programs is typically conservative. Furthermore, relying on static analysis will cause the system to become substantially dependent on the source language in which we write algorithmic policies.

## Slide 42: Trace Tree => Flow Table
tcpDst ==22
False
ethDst
2
drop
4
port 30
ethSrc
6
drop
True
match:{tcpDst!=22, ethDst:4,ethSrc:6}
match:{tcpDst!=22, ethDst:2}
match:{tcpDst==22}
Notes: The basic compilation algorithm is actually very simple, and we explain it here in the context of an example trace tree. For simplicity the leaves are labelled with switch-specific actions, such as forward on some ports or drop.
The basic algorithm generates one rule for each execution of f, and each execution of f is stored as a path from the root of the trace tree to a leaf. For example, the right-most path in this tree resulted from an execution that observed that tcpDst!=22 and ethDst==4 and ethSrc==6.
The leaf stores the action and the match condition can be obtained from the path from the root to the leaf. In this case, we would want to match on tcpDst!=22, ethDst==4 and ethSrc==6. Of course, as we described earlier, we cannot match on tcpDst!=22, and so instead we will generate a rule at some higher priority that matches on the condition which we wish to negate. This rule, which we call a “barrier rule” ensures that the rule for the execution which we are considering only fires when the condition is false.
We observe that all the rules that require tcpDst!=22 are under the False branch of the assertion node and all the rules that require tcpDst==22 are under the True branch of the assertion node. Therefore, we can determine the priority level of the barrier rule by first generating rules and assigning priorities to the False branch of the node, and then assigning the priority of the barrier rule to have the next higher priority. Then we can assign priorities to the True branch. Hence, by generating rules in-order from False to True, we can correctly assign priorities to rules.
Finally, since the subtree under the True branch may not completely describe how to handle all tcpDst==22 packets, some packets with tcpDst==22 may fall through to the reach the barrier rule. Therefore, the action for the barrier rule must be ToController, so that we can continue to trace f correctly.

## Slide 43: Trace Tree => Flow Table
tcpDst ==22
False
ethDst
2
drop
4
port 30
ethSrc
6
drop
True
match:{tcpDst!=22, ethDst:4,ethSrc:6}
Priority
match:{tcpDst==22}
action:ToController
barrier rule:
match:{tcpDst!=22, ethDst:2}
match:{tcpDst==22}
Notes: The basic compilation algorithm is actually very simple, and we explain it here in the context of an example trace tree. For simplicity the leaves are labelled with switch-specific actions, such as forward on some ports or drop.
The basic algorithm generates one rule for each execution of f, and each execution of f is stored as a path from the root of the trace tree to a leaf. For example, the right-most path in this tree resulted from an execution that observed that tcpDst!=22 and ethDst==4 and ethSrc==6.
The leaf stores the action and the match condition can be obtained from the path from the root to the leaf. In this case, we would want to match on tcpDst!=22, ethDst==4 and ethSrc==6. Of course, as we described earlier, we cannot match on tcpDst!=22, and so instead we will generate a rule at some higher priority that matches on the condition which we wish to negate. This rule, which we call a “barrier rule” ensures that the rule for the execution which we are considering only fires when the condition is false.
We observe that all the rules that require tcpDst!=22 are under the False branch of the assertion node and all the rules that require tcpDst==22 are under the True branch of the assertion node. Therefore, we can determine the priority level of the barrier rule by first generating rules and assigning priorities to the False branch of the node, and then assigning the priority of the barrier rule to have the next higher priority. Then we can assign priorities to the True branch. Hence, by generating rules in-order from False to True, we can correctly assign priorities to rules.
Finally, since the subtree under the True branch may not completely describe how to handle all tcpDst==22 packets, some packets with tcpDst==22 may fall through to the reach the barrier rule. Therefore, the action for the barrier rule must be ToController, so that we can continue to trace f correctly.

## Slide 44: Trace Tree => Flow Table
tcpDst ==22
False
ethDst
2
drop
4
port 30
ethSrc
6
drop
True
match:{tcpDst!=22, ethDst:4,ethSrc:6}
Priority
match:{tcpDst==22}
action:ToController
barrier rule:
match:{tcpDst!=22, ethDst:2}
match:{tcpDst==22}
Notes: The basic compilation algorithm is actually very simple, and we explain it here in the context of an example trace tree. For simplicity the leaves are labelled with switch-specific actions, such as forward on some ports or drop.
The basic algorithm generates one rule for each execution of f, and each execution of f is stored as a path from the root of the trace tree to a leaf. For example, the right-most path in this tree resulted from an execution that observed that tcpDst!=22 and ethDst==4 and ethSrc==6.
The leaf stores the action and the match condition can be obtained from the path from the root to the leaf. In this case, we would want to match on tcpDst!=22, ethDst==4 and ethSrc==6. Of course, as we described earlier, we cannot match on tcpDst!=22, and so instead we will generate a rule at some higher priority that matches on the condition which we wish to negate. This rule, which we call a “barrier rule” ensures that the rule for the execution which we are considering only fires when the condition is false.
We observe that all the rules that require tcpDst!=22 are under the False branch of the assertion node and all the rules that require tcpDst==22 are under the True branch of the assertion node. Therefore, we can determine the priority level of the barrier rule by first generating rules and assigning priorities to the False branch of the node, and then assigning the priority of the barrier rule to have the next higher priority. Then we can assign priorities to the True branch. Hence, by generating rules in-order from False to True, we can correctly assign priorities to rules.
Finally, since the subtree under the True branch may not completely describe how to handle all tcpDst==22 packets, some packets with tcpDst==22 may fall through to the reach the barrier rule. Therefore, the action for the barrier rule must be ToController, so that we can continue to trace f correctly.

## Slide 45: Trace Tree => Flow Table
tcpDst ==22
False
ethDst
2
drop
4
port 30
ethSrc
6
drop
True
match:{tcpDst!=22, ethDst:4,ethSrc:6}
match:{tcpDst==22}
action:ToController
Priority
barrier rule:
1
2
3
match:{tcpDst!=22, ethDst:2}
match:{tcpDst==22}
Simple, classical in-order tree traversal generates flow table rules!
Notes: The basic compilation algorithm is actually very simple, and we explain it here in the context of an example trace tree. For simplicity the leaves are labelled with switch-specific actions, such as forward on some ports or drop.
The basic algorithm generates one rule for each execution of f, and each execution of f is stored as a path from the root of the trace tree to a leaf. For example, the right-most path in this tree resulted from an execution that observed that tcpDst!=22 and ethDst==4 and ethSrc==6.
The leaf stores the action and the match condition can be obtained from the path from the root to the leaf. In this case, we would want to match on tcpDst!=22, ethDst==4 and ethSrc==6. Of course, as we described earlier, we cannot match on tcpDst!=22, and so instead we will generate a rule at some higher priority that matches on the condition which we wish to negate. This rule, which we call a “barrier rule” ensures that the rule for the execution which we are considering only fires when the condition is false.
We observe that all the rules that require tcpDst!=22 are under the False branch of the assertion node and all the rules that require tcpDst==22 are under the True branch of the assertion node. Therefore, we can determine the priority level of the barrier rule by first generating rules and assigning priorities to the False branch of the node, and then assigning the priority of the barrier rule to have the next higher priority. Then we can assign priorities to the True branch. Hence, by generating rules in-order from False to True, we can correctly assign priorities to rules.
Finally, since the subtree under the True branch may not completely describe how to handle all tcpDst==22 packets, some packets with tcpDst==22 may fall through to the reach the barrier rule. Therefore, the action for the barrier rule must be ToController, so that we can continue to trace f correctly.

## Slide 46: Handling User Inefficiency: Redundant Trace

## Slide 47: Example: Trace Reduction

## Slide 48: Example: Trace Reduction

## Slide 49: Example: Trace Reduction

## Slide 50: Example: Trace Reduction
Notes: SDN is a recent hot topic. During a recent NSF panel, many proposals are on SDN. A common feedback is if a propsal can be related with SDN.

## Slide 51: Example: Trace Reduction

## Slide 52: Example: Trace Reduction

## Slide 53: Flow Table Optimization

## Slide 54: Flow Table Optimization

## Slide 55: Flow Table Optimization

## Slide 56: Unnecessary Priority Levels

## Slide 57: Minimizing Priority Levels: Increasing at T Nodes Only

## Slide 58: Minimizing Priority Levels: Increasing at T Nodes Only

## Slide 59: Minimizing Priority Levels: Increasing at T Nodes Only

## Slide 60: Maple/Basic Runtime

## Slide 61: Maple/Basic Evaluation
3 real HP 5406 switches, client on one side, server on the other.
Client performs X HTTP reqs/s using httperf.
Measure average HTTP connection time as X varies.
Compare exact & maple
  Exact: up to 282 ms average
  Run-time: 1-2 ms: 100x reduction.
Notes: We measured the effect of using Maple-generated rules in a network using 3 real HP 5406 Openflow-enabled switches arranged in a linear topology. We connect a client and a web server on either side of the switches. The client issues HTTP requests to the web server and we measure the average HTTP connection time as we vary the rate at which HTTP connections are created at the client. We use an algorithmic policy that simple routes traffic based on the source and destination addresses. We compare the performance when using Maple’s rule generation method with the performance when generating only exact match rules and with the native L2 functionality of the switches.
We see that the performance of the exact match controller introduces substantial delay to the HTTP connection time, taking up to 282 ms when 120 requests are issued per second.
On the other hand, the Maple controller achieves a HTTP connection time of 2 ms at 120 requests per second, a 100x improvement. Maple’s performance closely matches that of the native L2 functionality up to about 100 requests per second.

## Slide 62: Evaluation: Maple as ACL Compiler
ACLs commonly used in network management
Questions
  How does one program ACL using Maple?
  How does one combine ACL with other policies, e.g. routing, load balancing?
Notes: To evaluate Maple, we apply it to an interesting problem: how to implement filter sets, such as access control lists that match on IP prefixes and TCP or UDP port ranges, on Openflow switches. This could be challenging, especially if we also want to solve the problem when the filter sets are combined with other policies, such as routing or load balancing policies.
We solve this problem with Maple by programming a simple filter set interpreter as an algorithmic policy, f.
The policy initially loads a filter set from a file, and then handles packets by just naively using the semantics of the filter set: iterate over filters in the filter set, test each filter against the packet and return an action based on the first matching filter.

## Slide 63: Maple Example: ACL+Routing
void insert(ACLItem acl, int pos, List<ACLItem> acls) {
acls.add(pos, acl);
}
void delete(int pos, List<ACLItem> acls) {
acls.remove(pos);
}
List<ACLItem> acls;
Route f(Packet p) {
if ( ! permit(p, acls) ) {
return null();
}
Location sloc = hostTable(p.ethSrc());
Location dloc = hostTable(p.ethDst());
Route path = myRoutingAlg(topology(),sloc,dloc);
return path;
}
boolean permit(Packet p, List<ACLItem> acls) {
for (ACLItem item : acls) {
if ( match(p, item) ) {
return item.action == PERMIT;
} }
return false;
}

## Slide 64: Benchmarking Compiler Quality
Benchmark: Classbench filter sets and packet traces for 3 filter set types - ACL, FW, IPC - and two sizes - 1000 and 2000 filters per filter set.
Metric: #priority levels used
Only 9 priority levels for 1000 rules
98 priority levels for 2000 IPC rules
Notes: In this graph we show the number of priority levels used by the Maple-generated rules for the same filter sets. We see that Maple often uses very few priority levels. For example, acl1a uses just 9 priorities for roughly 1000 rules. Some policies cause Maple to use substantially more priorities - for example acl2b required 120 priorities for nearly 2000 rules.

## Slide 65: Anatomy of a Network Control Function
Has physical states
f uses physical states
Map<MAC, Location> hostTable; List<ACLItem> acls;
Route f(Packet p) {
hostTable.put(p.ethSrc(), p.ingressPort());
if ( !permit(p, acls) ) return drop;
Location src = p.ingressPort();
Location dst = hostTable.get( p.ethDst() );
Route path = myRoutingAlg(topology(), src, dst);
return path;
}
Data path may need to detect change and update state
f uses policy state
Decision depends on pkt attributes
f depends on pkt attributes
External process may change the state
External process may change states

## Slide 66: Outline
Current SDN programming systems
Algorithmic SDN programming
  Programming model
  Maple
  Maple with auto-state-update
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 67: Implication
A general AP is a general function of the form:
f: (packet, state) (route, new-state, act)
When state changes, decision may change too.
If f() takes non-switch-implementable actions (e.g., causes state changes, sends packets), the packet should be punted back to the controller.
Notes: Maintaining correctness despite state changes is one of the key challenges of controller programming

## Slide 68: Existing Approaches on Handling State Dependency
Floodlight
  Wait for timeout of existing rules
  Problem: long delay; may not even be correct
Pyretic
  Completely rerun (a declarative) program and then compare the differences
  Problem: extreme low efficiency

## Slide 69: Maple/ASU: Goal
Can we introduce simple mechanisms so that we can achieve efficient (e.g., incremental) updates after state dynamics?

## Slide 70: Maple Mechanism
Only requirement: User program f uses simple library wrappers to access state variables
Reason: Provides both convenient data structures and importantly, again, decision dependency!

## Slide 71
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc =
hostTable(p.ethSrc());
Location dloc =
hostTable(p.ethDst());
Route path =
myRoutingAlg(
topology(),sloc,dloc);
return path;
}
}
EthSrc:1,
EthDst:2,
TcpDst:80
Assert: TcpDst==22
false
Read: EthSrc
1 (hostTable, 1)
Policy
Component | Traces
Dependency table (aka inverted index)
Notes: We use the example Java algorithmic policy to illustrate the tracing method. Suppose Maple executes the algorithmic policy on a packet with Ethernet source 1, Ethernet dest 2 and tcp destination 80. As the packet moves through the policy, Maple collects a trace of the execution.
When this packet arrives at the check on tcp destination, Maple records the assertion, and its outcome. In this case, the outcome is false. The program proceeds to the else branch, where it reads the source and destination addresses, both of which Maple logs. Finally, the program returns the computed path.

## Slide 72
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc =
hostTable(p.ethSrc());
Location dloc =
hostTable(p.ethDst());
Route path =
myRoutingAlg(
topology(),sloc,dloc);
return path;
}
}
EthSrc:1,
EthDst:2,
TcpDst:80
Assert: TcpDst==22
false
Read: EthSrc
1 (hostTable, 1)
Policy
Component | Traces
(hostTable,1) | [false, 1]
Dependency table (aka inverted index)
Notes: We use the example Java algorithmic policy to illustrate the tracing method. Suppose Maple executes the algorithmic policy on a packet with Ethernet source 1, Ethernet dest 2 and tcp destination 80. As the packet moves through the policy, Maple collects a trace of the execution.
When this packet arrives at the check on tcp destination, Maple records the assertion, and its outcome. In this case, the outcome is false. The program proceeds to the else branch, where it reads the source and destination addresses, both of which Maple logs. Finally, the program returns the computed path.

## Slide 73
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc =
hostTable(p.ethSrc());
Location dloc =
hostTable(p.ethDst());
Route path =
myRoutingAlg(
topology(),sloc,dloc);
return path;
}
}
EthSrc:1,
EthDst:2,
TcpDst:80
Assert: TcpDst==22
false
Read: EthSrc
Read: EthDst
1 (hostTable, 1)
2 (hostTable, 2)
Policy
Component | Traces
(hostTable,1) | [false, 1]
(hostTable,2) | [false, 1,2]
Dependency table (aka inverted index)
Notes: We use the example Java algorithmic policy to illustrate the tracing method. Suppose Maple executes the algorithmic policy on a packet with Ethernet source 1, Ethernet dest 2 and tcp destination 80. As the packet moves through the policy, Maple collects a trace of the execution.
When this packet arrives at the check on tcp destination, Maple records the assertion, and its outcome. In this case, the outcome is false. The program proceeds to the else branch, where it reads the source and destination addresses, both of which Maple logs. Finally, the program returns the computed path.

## Slide 74
Route f(Packet p) {
if (p.tcpDstIs(22))
return null();
else {
Location sloc =
hostTable(p.ethSrc());
Location dloc =
hostTable(p.ethDst());
Route path =
myRoutingAlg(
topology(),sloc,dloc);
return path;
}
}
EthSrc:1,
EthDst:2,
TcpDst:80
Assert: TcpDst==22
false
Read: EthSrc
Read: EthDst
1 (hostTable, 1)
2 (hostTable, 2)
Policy
topology
Component | Traces
(hostTable,1) | [false, 1]
(hostTable,2) | [false, 1,2]
topology | [false,1,2]
Dependency table (aka inverted index)
path1
Notes: We use the example Java algorithmic policy to illustrate the tracing method. Suppose Maple executes the algorithmic policy on a packet with Ethernet source 1, Ethernet dest 2 and tcp destination 80. As the packet moves through the policy, Maple collects a trace of the execution.
When this packet arrives at the check on tcp destination, Maple records the assertion, and its outcome. In this case, the outcome is false. The program proceeds to the else branch, where it reads the source and destination addresses, both of which Maple logs. Finally, the program returns the computed path.

## Slide 75: Example Dependency Table
Assert: TcpDsd==22
false
Read: EthSrc
path1
1
?
true
Read: EthDst
Read: EthDst
3
path2
4
2
(hostTable, 1)
(hostTable, 2)
(topology())
(hostTable, 3)
(hostTable, 4)
(topology())
Component | Traces
(hostTable,1) | [false, 1]
(hostTable,2) | [false, 1,2]
(hostTable,3) | [false, 3]
(hostTable,4) | [false, 3,4]
topology | [false,1,2],[false,3,4]
Dependency table (aka inverted index)

## Slide 76: Using Dependency Table
Assert: TcpDsd==22
false
Read: EthSrc
path1
1
?
true
Read: EthDst
Read: EthDst
3
path2
4
2
(hostTable, 1)
(hostTable, 2)
(topology())
(hostTable, 3)
(hostTable, 4)
(topology())
Component | Traces
(hostTable,1) | [false, 1]
(hostTable,2) | [false, 1,2]
(hostTable,3) | [false, 3]
(hostTable,4) | [false, 3,4]
topology | [false,1,2],[false,3,4]
Dependency table (aka inverted index)
host 4 changes location =>
Mark all relevant entries as need revalidation.

## Slide 77: Using Dependency Table
Assert: TcpDsd==22
false
Read: EthSrc
path1
1
?
true
Read: EthDst
Read: EthDst
3
path2
4
2
(hostTable, 1)
(hostTable, 2)
(topology())
(hostTable, 3)
(hostTable, 4)
(topology())
Component | Traces
(hostTable,1) | [false, 1]
(hostTable,2) | [false, 1,2]
(hostTable,3) | [false, 3]
(hostTable,4) | [false, 3,4]
topology | [false,1,2],[false,3,4]
Dependency table (aka inverted index)
host 4 changes location =>
Mark all relevant entries as need revalidation.
Background re-validation process re-runs packets at marked leaves.

## Slide 78: Maple/ASU Components

## Slide 79: Evaluations: Time to Recover from Failures
Maple: 6x,2x,3x improvement over Floodlight!

## Slide 80: Use Cases of ASU
Intent programming
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 81: Outline
Current SDN programming systems
Algorithmic SDN programming
  Programming model
  Maple
  Maple with auto-state-update
  Maple demo (Jason/Tony)
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 82: Maple Demo

## Slide 83: Outline
Current SDN programming systems
Algorithmic SDN programming
  Programming model
  Maple
  Maple with auto-state-update
  Maple demo (Jason/Tony)
  Problems of Maple using trace tree
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 84: Problems of Trace Tree
Quality: Compiles to a single flow table
Latency: A reactive approach that waits for punted packets to begin unfolding the trace tree and generating rules

## Slide 85: Why is Multi-Table Important for Quality (A Simple GBP Example)?
ethSrc
ethDst
a1
p1
a1
pn
an
ethDst
p
a1
pn2
an
ethSrc | ethDst | Action
a1 | a1 | p1
a1 | a2 | p2
.. | … | …
an | an | pn2
Assume n hosts in hostTable
TT after pingall among the n hosts
Flow table from trace tree
n2 entries
Map<MAC, ConditionSet> hostTable;
0. Route onPacketIn(Packet p) {
1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
2. ConditionSet dstCond = hostTable.get( p.ethDst() );
3. if (srcCond != null && dstCond != null && pass(srcCond, dstCond) )
4. return pass;
5. else
return drop; }

## Slide 86: More Efficient Multi-Table (2 Tables) Design
Table 1
Table 2
ethSrc | Action
a1 | regsrcCond=y1 jump 2
a2 | regsrcCond=y2 jump 2
.. | …
an | regsrcCond=yn jump 2
otherwise | drop
regsrcSw | ethDst | Action
y1 | a1 | p1,1
y1 | a2 | p1,2
.. | … | …
yk | an | pk,n
otherwise |  | drop
n + kn entries
Assume k condition possibilities.

## Slide 87: More Efficient Multi-Table (3 Tables) Design
Table 1
Table 2
ethSrc | Action
a1 | regsrcCond=y1 jump 2
a2 | regsrcCond=y2 jump 2
.. | …
an | regsrcCond=yn jump 2
otherwise | drop
regsrcCond | regsdstCond | Action
y1 | y1 | p1,1
y1 | y2 | p1,2
.. | … | …
yk | yn | pk,k
otherwise |  | drop
2n + k2 entries
Assume k condition possibilities.
ethDst | Action
a1 | regdstCond=y1 jump 3
a2 | regdstCond=y2 jump 3
.. | …
an | regdstCond=yn jump 3
otherwise | drop
Table 3
Assume n = 4000, k = 100 n2: 1,000,000 = 1000K 2.5x n+kn: 4,000 + 400,000= 404K 22x
2n + k2: 8000 + 10,000 = 18K

## Slide 88: Outline
Current SDN programming systems
Algorithmic SDN programming
  Programming model
  Maple/TT (aka Maple 1.0)
  Maple/TT+auto-state-update (aka Maple 1.5)
  Maple demo (Jason/Tony)
  Problems of Maple using trace tree
  USTC Multi-table for POP [Xinyu Feng, Chunhui’2015]
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 89: Add Slides on USTC/POP

## Slide 90: Outline
Current SDN programming systems
Algorithmic SDN programming
  Programming model
  Maple/TT (aka Maple 1.0)
  Maple/TT+auto-state-update (aka Maple 1.5)
  Maple demo (Jason/Tony)
  Problems of Maple using trace tree
  USTC Multi-table for POP [Xinyu Feng, Chunhui’2015]
  Magellan
Notes: At a high level, abstraction is to hide issues that others do not want to or hard to do things.

## Slide 91: Magellan: Ideal Design Goal
Proactively, fully generate flow tables
Problem
  Switch has limited computation model
    Execution paths that lead to non-switch-implementable actions (e.g., state update) still need to punt
    Flow-table-unfriendly instructions may need to be punted as well

## Slide 92: An Example FT-Friendly AP
blockPort = 22 // policy
servers = [A, B, C, D] // net func hostTable = {A:0,B:1,C:2,D:3} // netview
def onPacketIn(p): // policy+netfunc+netvw -> DP
if blockPort == p.tcp_dst: return drop
else: s = servers[p.ip_src % len(servers)]
return forward([hostTable[s]])

## Slide 93: An Example FT-Unfriendly AP
blockPort = 22 // policy
servers = [A, B, C] // net func hostTable = {A:0,B:1,C:2,D:3} // netview
def onPacketIn(p): // policy+netfunc+netvw -> DP
if blockPort == p.tcp_dst: return drop
else: s = servers[p.ip_src % len(servers)]
return forward([hostTable[s]])
3 instead of 4 servers
There is no compact representation of instruction pkt-attr % k, where there is no i. s.t. k = 2i.

## Slide 94: Magellan: Realistic Goals and Basic Ideas
Maximize flow table hit using minimal flow table size
Basic idea:
  Trace tree is a mostly blackbox approach, while Magellan starts with the other extreme---a whitebox approach.

## Slide 95: Magellan: Basic Ideas
Function f consists of a sequence of instructions (in an intermediate representation) I1, I2, …, In.
Each instruction I is a mapping from input variable states to output variable states
InVar(I)1 | InVar(I)2 | InVar(I)3 | OutVar(I)
1 | 1 | 1 | OutVar(I)=I(1,1,1)
… |  |  | 
… |  |  | 

## Slide 96: Example
Map<MAC, ConditionSet> hostTable;
0. Route onPacketIn(Packet p) {
1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
2. ConditionSet dstCond = hostTable.get( p.ethDst() );
3. if (srcCond != null && dstCond != null && pass(srcCond, dstCond) )
4. return port1;
5. else
return drop; }
Map<MAC, ConditionSet> hostTable;
Route onPacketIn(Packet p) {
I1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
I2. ConditionSet dstCond = hostTable.get( p.ethDst() );
I3. branch [srcCond != null && dstCond != null && pass(srcCond, dstCond) ] I4 I5
I4. return port1
I5. return drop

## Slide 97: Example
p.ethSrc | Action
1 | srcCond1 jump I2
2 | 
... | 
248 | srcCond2^48 jump I2
srcCond | dstCond | Action
srcCond1 | dstCond1 | jump I4
… |  | jump I5
… |  | 
I1
p.ethDst | Action
1 | dstCond1 jump I3
2 | 
... | 
248 | dstCond2^48 jump I3
I2
I3
Map<MAC, ConditionSet> hostTable;
Route onPacketIn(Packet p) {
I1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
I2. ConditionSet dstCond = hostTable.get( p.ethDst() );
I3. branch [srcCond != null && dstCond != null && pass(srcCond, dstCond) ] I4 I5
I4. return port1
I5. return drop

## Slide 98: Problem of Naïve Table Mapping
p.ethSrc | Action
1 | srcCond1 jump I2
2 | 
... | 
248 | srcCond2^48 jump I2
I1
Table construction does not consider available state info: only the n values in current hostTable state are needed. Hence table size should be n+1, not 248
I1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
p.ethSrc | Action
a1 | srcConda1 jump I2
a2 | 
.. | …
an | srcCondan jump I2
otherwise | srcCond=null
We say I1 is a compact-mapable (CM) statement.

## Slide 99: More Examples of CM Statements
p.ethSrc | Action
1 | y=false
... | 
m | y=false
m+1 | y=true
… | …
248 | y=true
y = p.ethSrc() > m
p.ethSrc | Action
… | …
y = p.ethSrc != p.ethDst
p.ethSrc | p.ethDst | Action
p.ethSrc | p.ethDst | Action
1 | 1 | y=false
1 | 2 | y=true
... | ... | …
248 | 248 | y=true

## Slide 100: CM Propagation through Data-Flow Analysis
I1 (hostTable)
ethSrc
srcCond
I2 (hostTable)
ethDst
dstCond
I3
route
ethSrc | Action
A | Reg1 = 01; jump T2
Reg1 | Reg2 | Action
01 | 02 | route
ethDst | Action
B | Reg2 = 02; jump T3
Instructions
100
Map<MAC, ConditionSet> hostTable;
Route onPacketIn(Packet p) {
I1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
I2. ConditionSet dstCond = hostTable.get( p.ethDst() );
I3. branch [srcCond != null && dstCond != null && pass(srcCond, dstCond) ] I4 I5
Limited by hostTable.values()

## Slide 101: CM Propagation through Data-Flow Analysis
p.ethSrc | Action
a1 | srcConda1 jump I2
a2 | 
... | 
an | srcCondan jump I2
srcCond | dstCond | Action
srcCond1 | dstCond1 | y=true; jump I4
… |  | y=false; jump I5
… |  | 
I1
p.ethDst | Action
a1 | dstConda1 jump I3
a2 | 
... | 
an | dstCondan jump I3
I2
I3
Map<MAC, ConditionSet> hostTable;
Route onPacketIn(Packet p) {
I1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
I2. ConditionSet dstCond = hostTable.get( p.ethDst() );
I3. branch [srcCond != null && dstCond != null && pass(srcCond, dstCond) ] I4 I5
I4. return port1
I5. return drop
Only output in I1/I2 tables are needed as input to I3 table input

## Slide 102: Map -> Map-Explore
Map<MAC, ConditionSet> hostTable;
Route onPacketIn(Packet p) {
I1. ConditionSet srcCond = hostTable.get( p.ethSrc() );
I2. ConditionSet dstCond = hostTable.get( p.ethDst() );
I3. branch [srcCond != null && dstCond != null && pass(srcCond, dstCond) ] I4 I5
I4. // path = shortest path alg to compute route // from p.ingressSw to ethDst
return path
I5. return drop

## Slide 103: Magellan: Optimizations
One table per instruction may generate too many tables. One can merge tables from multiple instructions.
Map<MAC, int> table;
Route onPacketIn(Packet p) {
I1. int val1 = table.get( p.ethSrc() );
I2. int val2 = val1 * val1;
I3. branch [val2 > 10] I4 I5
I4. return pass
I5. return drop
I2 can merge w/ I1.
Consider I2, which follows I1. If input(I2)=input(I1,I2), then merge them will not increase table size.

## Slide 104: Magellan: Main Components and Workflow
IR
Compile
Analyze& Design
Code Gen
static compile
time
Explorer Graph
Explorer
dynamic run
time
Packets Notifications
Rules
Table Graph
onPacket
DB
Openflow switch
P4 switch
P4 Pipeline
Northbound
FlowRule Compile

## Slide 105: Status
Ongoing systems
  Maple (Java, ODL, Single table)
  USTC/XXX name (C, POP)
  Maple with table compression/annotation (multi-tables)
  Magellan

## Slide 106: Thank You

## Slide 107: A Simple ScienceNET Example Controller
badSrc = 100 // policy topo = {…} // netview
def onPacketIn(p): // policy+netvw->DP
if badSrc == p.ip_src: return drop
else: return mySNAlg(topo, p.ip_dst)
def mySNAlg(topo, dst-ip):
if dtn.ip == dst-ip: return alg1(topo, dst-ip)
else: return alg2(topo, dst-ip)
D (dtn)
A
B

## Slide 108: End Result: Flow Table
Priority | ip_src | ip_dst | Action
1 | 100 | * | drop
0 | * | A | out 2
0 | * | B | out 2
0 | * | D | out 1
Table has many wildcard entries => inefficient.
D
A
B

## Slide 109: More Efficient Flow Tables using OF 1.3
ip_src | Action
100 | drop
default | Jump Table 2
ip_dst | Action
A | out 2
B | out 2
D | out 1
Table 1
Table 2
D
A
B

## Slide 110: Software Architecture w/ Network Program Lang
Admin/UI
Infrastructure Layer
Southbound
Service/App
ACL
Service Chain
L3/2 VPN
PhysicalView
AbstractViews
fACL
fService Chain
fL3/2 VPN
DeviceModel
Shortest Path
f…
Packet-Processor-Independent Processing
DeviceModel
DeviceModel
Automatic generate memorization tables; capture (closure) and maintain consistency w/ state
110

## Slide 111: A Simple ScienceNET Example Controller
badPort = 22 // policy topo = {…} // netview
def onPacketIn(p): // policy+netvw->DP
if badPort == p.tcp_dst: return drop
else: return myRtAlg(p.eth_dst)
def myRtAlg(eth_dst):
if dtn.eth == eth_dst: return alg1(topo, eth_dst)
else: return alg2(topo, eth_dst)
D (dtn)
A
B

## Slide 112: An Evolution View of Intradomain Routing Toward SDN
Datapath
Distributed Bellman Ford
Datapath
Distributed Bellman Ford
Datapath
Distributed Bellman Ford
Distance Vector
Datapath
Distributed Link State
Datapath
Distributed Link State
Datapath
Distributed Link State
Link State
Dijkstra
Dijkstra
Dijktra
Notes: RIP: 1988 RFC1058 RFC2328

## Slide 113: An Evolution View of Intradomain Routing Toward SDN
Datapath
Distributed Link State
Datapath
Distributed Link State
Datapath
Distributed Link State
Link State
Dijkstra
Dijkstra
Dijkstra
Datapath
Datapath
Control
Datapath
SDN
standard control
protocol
Link State
Notes: FLP, Arrow’s Impossibility Theorem. Failure of distributed computing.

## Slide 114: Status
Two implementations
Maple
A reactive (dynamic-tracing) blackbox approach that demonstrated the basic feasibility of automating programming
Code will become openly available in OpenDaylight as part of CCIIE
Test deployment at Yale ScienceNet
Magellan (aka Maple 2.0)
A general view that a centralized algorithmic policy (AP) is a stream processing function
A whitebox approach where distributed network flow tables are memorization tables implementing algorithmic policies
In active design and implementation phase